## Slide 1: DSP LAB EXPERIMENT -03 Study of application autocorrelation function for analysis of signals
Priya
17EE01044

## Slide 2: Autocorrelation
Serial correlation
correlation of the signal with the delayed version of itself as the function of the delay
Rm=
Aim
Computing pulse rate (PR) from a PPG signal and pitch period of a speech signal using autocorrelation
function (ACF) in real time Arduino prototype platform.
Theory
Where m=0,1,2....... N-1

## Slide 3: Properties
Even function
mathematical tool for finding repeating patterns
determine the periodicity of the signal having noise.
recognition and detection purpose

## Slide 4: Schematic
Ppg+noise signal/audio signal
Moving average filter
Mean removal
Autocorrelation
Zero crossing, Pitch
Period calculation
Normalization
  Lmax1 = FZCP + Lmax.
P = Lmax1 / Fs. (Fs=100)
FZCP->first zero crossing value
Lmax1->peak instant after FZCP